## Slide 1: Forensic
Toxicology &
Uncertainty in medical testing

## Slide 2: Toxicology
The study of the adverse effects of chemicals on living organisms
Forensics involve illegal drug use, drug abuse, poisons and death
Specimens are collected and analyzed in a toxicology lab (blood, urine, saliva, vitreous humor, stomach contents, etc)

## Slide 3: Death investigations
It is necessary to document the “chain of custody” for all specimens as the results can be submitted as evidence in court.

## Slide 4: What tests are performed?
Depends on the initial screening.
Specimens can be tested for up to 300 different drugs and potential poisons.
Once toxin is detected, more advance testing is done.

## Slide 5: Chromatography
Is the separation of a mixture of chemicals (chromatography)
Different chemicals in the sample move through the chromatograph at different speeds and thus exit at different times
Afterwards it is directed to the mass spectrometer, where it is hit with a beam of electrons.
Each chemical breaks up into a different set of particles with a different pattern.

## Slide 6
These patterns are compared to a database of spectra of more than 700,000 different compounds to identify the toxin

## Slide 7: Challenge
Illegal drugs are being created constantly with slight changes in chemistry and they can evade this detection and identification system.

## Slide 8: Gas Chromatographs
Super sensitive but require careful calibration prior to use to ensure accuracy.
Requires high temperatures to volatilize the substance so the sample can be analyzed
It is expensive to operate and requires advance training
NC has one Forensic Toxicology lab that offers this.

## Slide 9: Liquid Chromatography
Can use smaller samples
Requires less advance prep of sample
Sample does not require high temperatures like the gas chromatograph
More accessible

## Slide 10: Common chemicals screened:
Amphetamine
Codeine
Diacetylmorphine (heroin)
Methamphetamine
Morphine
Oxycodone
Tetrahydrocannabinol (marijuana)

## Slide 11: Uncertainty in Medical tests
Diagnostic and forensic tests are often accurate but there is a certain amount of predictable inherent error.
This is often underestimated which can have serious medical and legal consequences

## Slide 12: Types of error
True positive: when a test shows positive for a condition or disease that is truly present.
False positive: when a test shows something that isn’t really there.

## Slide 13
True negative: when a test shows negative for a condition that really isn’t present
False negative: is when a test fails to detect a condition that a person really has.

## Slide 14
False negatives and false positives can be most problematic.
Why?
FDA requires companies that develop and manufacture diagnostic tests to determine the sensitivity and specificity of these tests.

## Slide 15: Sensitivity and Specificity
Sensitivity is the measure of how often a test will detect a condition when the condition is present
  Sensitivity = TP / (TP + FN)
Specificity is the measure of how often a test will give negative results for a condition when the condition is not present
  Specificity = TN / (TN + FP)

## Slide 16: Sources of error
Medical lab professionals work hard to minimize errors in the lab, errors still exist at every stage:
  Collecting
  Labelling
  Reporting results
  Quality controls out of range

## Slide 17
Labs perform error analysis to figure out process problems so that they can minimize these errors.
Diagnoses should be taking into consideration ALL the critical sources of patient information:
  Patient interview, physical exam, medical history and medical tests